## Slide 1
B.TECH PROJECT END-EVALUATION
Design and development of fully automated biaxial stretching mechanism for dielectric elastomers
Presented by :
Pranshu Devlia - 230003052
Jitesh K. Meena - 230003030
Guided by :
Dr. Aman Khurana
Assisstant Professor
Department of Mechanical Engineering
IIT Indore

## Slide 2
CONTENT :
  Introduction
  Significance of Pre-stretch
  Existing Mechanisms
  Objective
  Work Done
  Design and Measurements
  Hardware Components
  Block and Circuit Diagram
  Future Work
o

## Slide 3
Maxwell stress
INTRODUCTION : DIELECTRIC ELASTOMERS
  Large deformations
  Efficient Electromechanical coupling
  Soft, flexible & lightweight
Applications :
Actuators • Sensors • Energy Harvesters • Haptic Devices • Acoustic Transducers • Pneumatic Valves • Wearable Systems • Power Generators • Soft Robotics
Properties :
At excessive thinning excessive electric field
further thinning
↓
Positive Feedback Loop
↓
EMI → rapid unstable thinning → electrical breakdown
Challenege :

## Slide 4
SIGNIFICANCE OF PRE-STRETCH :
Equi-biaxial
Actuation Ratio v/s Voltage at different pre-stretches & different stretching modes. [4.],[5.]
  Strain Stiffening
  Suppresses EMI
  Greater Actuation Range
  Lower Voltage requirements

## Slide 5
EXISTING MECHANISMS :
Biaxial Planar Testing Device with Load Cell & multi-turn potentiometer sensors
Has uni/biaxial mode selection switch and computerised parametric selection
Limitations : Uses Non-compliant Fixtures , changes Orientation absurdly
Ref. Dilshad Ahmad, Sujit Kumar Sahu, and Karali Patra (2019)
Fracture toughness, hysteresis and stretchability of dielectric elastomers under equibiaxial and biaxial loading.
Polymer Testing, Volume 79, 106038.
Traditional heavy setups for tensile stretching

## Slide 6
EXISTING MECHANISMS :
Ref. Paul White, Stella Latscha, and Mark Yim (2014).
Modeling of a Dielectric Elastomer Bender Actuator.
Actuators, Volume 3, pp. 245–269.
Manual biaxial stretching device based on slider setup
Limitations : Purely Manual, Uses Non-Compliant Fixtures, Orientation changes absurdly.
Semi-Automated equibiaxial pre-stretching roller-slider machine
Limitations : Not fully automated, Uses Non-Compliant Fixtures, Orientation changes absurdly , user has to rely on physical distance markings to achieve desired stretch.
Ref. Yuanlin Guan, Ziyin Liu et. al. (2026).
Research on design of soft gripper by dielectric elastomer actuator based on quadrangular star honeycomb support.
PLOS ONE, Volume 21, Issue 7, e0352654..

## Slide 7
EXISTING MECHANISMS :
Ref. Luo Z. et al. (2024).
A biaxial pre-stretching device and method for multi-shape dielectric elastomer samples.
Chinese Patent CN117825122B
Manual biaxial stretching device based on roller slider setup
Limitations : Purely Manual, Uses Non-Compliant Fixtures, Orientation changes absurdly.
Vacuum based Biaxial Cell stretcher
Limitations : Needs constant power supply to keep it stretcehd, No mechanical lock, Orientation changes absurdly, Cannot give unequal biaxial stretch, Non uniform stretching.
Ref. Jue Wang, Aritra Chatterjee et. al. (2024).
Pneumatic Non-Equibiaxial Cell Stretching Device With Live-Cell Imaging
IEEE Transactions on Biomedical Engineering, 71(3), 820–830.

## Slide 8
EXISTING MECHANISMS :
Ref. Sze-Hsien Low and Gih-Keong Lau (2014).
Bi-axially crumpled silver thin-film electrodes for dielectric elastomer actuators.
Smart Materials and Structures, Volume 23, Issue 12, 125021.
Clips based Radial stretcher
Limitations : Semi-automatic , manual locking
Radial Stretcher with Camera based Feedback
Paper not informative enough to conclude limitations.
Ref. Simon Holzer, Bhawnath Tiwari et. al. (2025).
Design and Characterization of an Equibiaxial Multi-Electrode Dielectric Elastomer Actuator.
Materials, Volume 18, 1693.

## Slide 9
EXISTING MECHANISMS :
Fully Automated Radial Stretching Mechanism with self-locking and direct user input.
Ref. SMILE Lab IITI (2025)
Design and Development of an Automated Radial Stretching Mechanism for Elastomeric Membrane.
B.Tech. Project Report, IIT Indore, 2025
Manual → Motorized Testing Mechanisms → Feedback-Assisted
→ Semi-Automated Biaxial Stretching → Fully Automated Radial Stretching → Towards Fully Automated X–Y Biaxial Stretching Mechanism

## Slide 10
Design Features :-
  Motorized actuation with controlled feedback
  Automated positioning
  Independent X–Y biaxial stretch control
  Direct User-defined stretch ratios as input
  Easy-to-operate Screen Menu with simple buttons
  Compact and integrated mechanism
  Reliable longer duration pre-stretch self locking without unnecessary power consumption
  Low-cost fabrication using 3D-printed components and electronics
  Compliant fixtures that keep the orientation of DE intact
  Unifrom Stretching & Repeatability
  Stretch-ratio resolution of 0.01x of original dimensions
OBJECTIVE :
To develop a fully automated biaxial stretching mechanism for DE.

## Slide 11
DESIGN :
  Design idea & Parts measurements
  3D-modelling of all the components in Autodesk Fusion
  Assembly of parts & motion simulation in Fusion
  Tolarences testing & Design corrections
  3D printing of the complete parts to check functionality
WORK DONE :
HARDWARE :
  Understanding the Hardware requirements
  Finalising the electronic components
  Planning the signal flow
  Plotting the Final Circuit
AUTOMATION :
  Rough Arduino UNO code for UI, display & buttons
  Partial Arduino MEGA framework for motion control
  Established UNO <--> MEGA communication code

## Slide 12
INITIAL DESIGNS :
Limitations :
4-pins mechanism
Higher stress concentration
Sqaure Nut-Bolt slider mechanism required at Pins
Frequent Neck design usage
Weak Resistance against Bending
Animation

## Slide 13
INITIAL DESIGNS :
Limitations :
4-pins mechanism
Higher stress concentration
Non-uniform rotary load distribution between 2 base gears
Requires a lot of constraining fences & blocks designs.

## Slide 14
FINAL DESIGN :
Advantages :
8-pins mechanism
Uses scissor design to mediate between pins and elastomer.
Lower stress concentration & uniform stress distribution across the elastomer.
Compact and effective constraints in design.
Easier hardware integration

## Slide 15
FINAL DESIGN :

## Slide 16
8-PIN SCISSOR MECHANISM :
Acts as a compliant fixture

## Slide 17
EXPLODED DESIGN VIEW :
Upper T Base + Source Gear with Motor + T Rack
X Direction
Central Gears 1 & 2 + Motors
Cross L Racks
Y Direction
Lower Base for Hardware Integration
Rack Gear Mechanism
Scissor Mechanism + DE

## Slide 18
IMPORTANT DESIGN MEASUREMENTS :
Gears :
Module = 2
Pressure Angle = 20°
No. of Teeth = 28
Pitch radius = 14 mm
Thickness = 28 mm
Cross L Racks :
Module = 2
Pitch = 2π = 6.28 mm
No. of Teeth = 63
Length = 400.6 mm
Width = 20 mm
Thickness = 30 mm
T Rack :
Module = 2
Pitch = 2π = 6.28 mm
No. of Teeth = 66
Length = 419.44 mm
Width = 50 mm
Thickness = 30 mm
Tolerances between :
Rack Teeth & Walls = 0.4 mm
2 Walls = 0.4 mm
Rack Teeth & Gear Teeth = 0.15 mm
Rest was designed accordingly
T Base :
Length = 410 mm
Width = 238 mm

## Slide 19
HARDWARE COMPONENTS :
12V SMPS Adapter
Arduino Uno
Arduino Mega
Limit Switch
(NO)
Terminal Block
LCD
Display
5V Buck
Converter
Rotary Encoder
Motor
Driver
DC Worm Gear Motor
with encoder
Fuse
Switch
Back Button

## Slide 20
Electrical Power
Electrical Signal
Mechanical Transmission
Motor Driver
Motor + Encoder
Mechanism
Limit Switch
Gear Box
AC Power Source
LED Display
Rotary Encoder
12V SMPS
5V Buck Converter
Microcontrollers
(Uno Mega)
Back
Button
BLOCK DIAGRAM :

## Slide 21
CIRCUIT DIAGRAM :

## Slide 22
FUTURE WORK :
Hardware Testing
Motor & Encoder Caliberation
Design Modification
Final Parts Fabrication
Hardware Integration
Wire Connections
Model Testing and Rectifications

## Slide 23
REFERENCES :
[1.] Bo Li, Hualing Chen, Junhua Qiang, Shulin Hu, Zicai Zhu and Yongquan Wang (2011)
Effect of mechanical pre-stretch on the stabilization of dielectric elastomer actuation.
Journal of Physics D: Applied Physics, 44, 155301.
DOI: 10.1088/0022-3727/44/15/155301
[2.] Liang Jiang, Anthony Betts, David Kennedy and Stephen Jerrams (2016)
Eliminating electromechanical instability in dielectric elastomers by employing pre-stretch.
Journal of Physics D: Applied Physics, 49, 265401.
DOI: 10.1088/0022-3727/49/26/265401
[3.] Deepak Kumara, Somnath Sarang (2020)
Pre-stretching effect modeling of a dielectric elastomer under the electrical loading condition.
Materials Today: Proceedings, 24, 290–297.
DOI: 10.1016/j.matpr.2020.04.278
[4.] Danh Quang Tran , Jin Li , Fuzhen Xuan and Ting Xiao (2018)
Viscoelastic effects on the actuation performance of a dielectric elastomer actuator under different equal, un-equal biaxial pre-stretches. *
Materials Research Express, 5, 065303.
DOI: 10.1088/2053-1591/aac673
[5.] Ajeet Kumar , Dilshad Ahmad , Karali Patra (2018)
Dependence of Actuation Strain of Dielectric Elastomer on Equi-biaxial, Pure Shear and Uniaxial Modes of Pre-stretching. *
IOP Conference Series: Materials Science and Engineering, 310, 012104.
DOI: 10.1088/1757-899X/310/1/012104

## Slide 24
THANK YOU !